## Slide 1
Particle‒wall interaction
Case I
V
F I
Case II
V
F II
The distance to the wall is the same in both cases
Intuitively, one can say |F I| > |F II| since in Case I the particle is moving towards the wall. This, indeed, holds true if we take inertia of the fluid into account. However, the Stokes regime implies that inertial effects are neglected. See a more detailed explanation in Section 4 (Discussion) of: “Brenner, H. The slow motion of a sphere through a viscous fluid towards a plane surface. Chem. Eng. Sci., 16(3-4), 242-251 (1961)”
Q1: |F I| = |F II| a) > b) = c) <
Interaction in Stokes regime

## Slide 2
Particle‒wall interaction
V
F
T
A particle translating along an infinite rigid plane
Q2: F a) upwards ↑
b) downwards ↓
Q3: T a) CW ↻
b) CCW ↺
Disturbance generated by a particle moving in a viscous fluid
The Stokes disturbance field induced by a single particle translating in a viscous flow is shown in the figure above. The disturbance has a net force acting on the wall as if it wants to push it upwards. Since the wall is stationary, it has an equal opposite reaction whose reflection at the location of the particle generates a downwards force and a clockwise torque. Note that the wall reaction ↓ is added to the viscous drag ↓ acting on the particle (−6πμaV) which exists even if there is no wall.
Disturbance of V at the wall
Wall reaction
Wall reaction effect on the particle
Interaction in Stokes regime

## Slide 3
Particle‒wall interaction
Ω
F
T
Q4: F a) upwards ↑
b) downwards ↓
Q5: T a) CW ↻
b) CCW ↺
A particle rotating along an infinite rigid plane
Disturbance of Ω at the wall
Wall reaction
Note that the wall reaction ↺ is added to the viscous drag ↺ acting on the particle (−8πμa³Ω) which exists even if there is no wall.
Disturbance generated by a particle rotating in a viscous fluid
Interaction in Stokes regime

## Slide 4
Particle‒particle interaction
Q6: |F1| = |F2| a) > b) = c) <
V
V
a1 = a2
A pair of particles following each other along their line of centers
Intuitively, one can say |F1| < |F2| since the 1st particle is in the wake of the 2nd one. This, indeed, holds true if we take inertia of the fluid into account. However, the Stokes regime implies that inertial effects are neglected. Therefore, the viscous forces and reflections/reactions Fαα (discussed in the first slide: reaction of pushing the non-moving 2nd by 1st = reaction of pulling the non-moving 1st by the 2nd) as well as the disturbances Fαβ (pulling 1st by 2nd = pushing 2nd by 1st) are equal. See more details in: “Stimson, M., & Jeffery, G. B. The motion of two spheres in a viscous fluid. Proc. R. Soc. Lond. Ser. A, 111(757), 110-116 (1926)”
Push by 1st
Hint: F1 = F11 + F12 & F2 = F22 + F21
Fαα: The viscous drag acting on particle α due to its translation at Vα next to the non-moving spherical particle β (= 3 ‒ α)
Fαβ: The disturbance due the translation of particle β at Vβ felt by particle α (= 3 ‒ β)
Pull by 2nd
F12 = F21
F11 = F22
Interaction in Stokes regime
2
1
Reactions

## Slide 5
Particle‒particle interaction along their line of centers
Interaction in Stokes regime
λ = 1
λ = 0.5
λ = a2 / a1
ξ = 2h / (a1 + a2)
h = gap

## Slide 6
Particle‒particle interaction
V
V
Case I
F1
T1
V
V
Case II
Q11: |F1I| < |F1II| a) > b) = c) <
Q12: |T1I| < |T1II| a) > b) = c) <
Q7: F1I | a) upwards ↑
 | b) downwards ↓
Q8: T1I | a) CW ↻
 | b) CCW ↺
Q9: F1II | a) upwards ↑
 | b) downwards ↓
Q10: T1II | a) CW ↻
 | b) CCW ↺
A pair of particles translating normal to their line of centers
Hint: F1 = F11 + F12 & T1 = T11 + T12
Note: due to symmetry Fi & Ti are equal for particles
The distance is the same in both cases
F11 (reflection of V1 reaction
+ viscous force from V1) > F12
Disturbance of V1
Reaction
F12 from V2
For these questions the values of resistances, given in Table 1 of O'Neill‒Majumdar (1970) ZAMP paper, are needed for the cases where the interaction forces/torques are in opposite directions.
T12 from V2
T11
T12
T11
F11
F12
F1
T1
Interaction in Stokes regime

## Slide 7
Particle‒particle interaction normal to their line of centers: translation
Interaction in Stokes regime

## Slide 8
Particle‒particle interaction
Q17: |F1I| > |F1II| a) > b) = c) <
Q18: |T1I| > |T1II| a) > b) = c) <
Case I
Case II
Q13: F1I | a) upwards ↑
 | b) downwards ↓
Q14: T1I | a) CW ↻
 | b) CCW ↺
Q15: F1II | a) upwards ↑
 | b) downwards ↓
Q16: T1II | a) CW ↻
 | b) CCW ↺
A pair of particles rotating normal to their line of centers
Ω
Ω
Ω
Ω
Note: due to symmetry Fi & Ti are equal for particles
T11
F11
F12
F1
T1
T12
F11
F12
T1
F1
Exception! depends on λ
The distance is the same in both cases
T11
T12
Interaction in Stokes regime
For these questions the values of resistances, given in Table 1 of O'Neill‒Majumdar (1970) ZAMP paper, are needed for the cases where the interaction forces/torques are in opposite directions.
Hint: F1 = F11 + F12 & T1 = T11 + T12

## Slide 9
Particle‒particle interaction normal to their line of centers: rotation
Interaction in Stokes regime